## Slide 1: DC Wall Box
HMI – IMX 8M plus

## Slide 2: SW component inside iMX – Phytech board
DC Wall box – Connectivity proposal
Display Unit
Data Interface Engine
  module derives insights/ conclusions from the input data CAN inputs
  Publishes data to be displayed on display unit via MQTT
  Forwards event info from display unit to CAN API block for generating CAN frames
CAN API block
  Provides wrapper APIs for CAN send and receive messages
    Eg: getCAN(ID), setCAN(ID)
Native CAN Driver
  OS supported CAN driver
CAN API –
Send/ Receive
Native CAN driver
charcon
Vsec
CAN Bus
Display Unit
Data Inference Engine
MQTT
API Calls
iMX Board

## Slide 3: Subcomponent -- SW subsets
DC Wall box – Connectivity proposal
CAN
CAN Dumps
Data Handling
MQTT
MQTT Broker
What to Pub/ Sub?
GSM
  Bringing GSM up using APN codes – Auto detection
API
Send
Receive
CAN health Check
Startup
HIVE MQTT
Data Interface Engine
Compute function outputs – Hypothesis
  Ping test periodically
  GSM time for display
OTA
CAN Interface
MQTT interface
Pub/ Sub to HMI application
Comm to low level CAN API
Handle Event from HMI
Event to CAN
  HMI App
  Data Interface Engine
HMI
LVGL
Operating System
Yocto Linux
IMD
  Digital input output read
Cloud
Solar Irradiation – Mechanism to fetch this data
Logging
Event Management
Variable Mapping
Event Pub/ Sub
UI team for Graphic development
Image handling
License open source
Startup scheduling
Scheduling sequence of Data interface Engine and HMI app
  PWM for understanding the system state
Export longs
SW update
System Logger
CAN Dumps
Data Interface Engine logging
HMI logging*
HMI Team
Collaborative
TBD
Workshop on Work package analysis (5th Sep): PJ-CSS, EHM-PD3-PJ3
Identified key work package
SW component discretization
Development Language
  Data Interface Engine – Python
  HMI – C++
MQTT broker
  HIVE MQTT
HMI
  LVGL

## Slide 4: Subcomponent -- SW subsets –plan for CW37
DC Wall box – Connectivity proposal
CAN
CAN Dumps
Data Handling
MQTT
MQTT Broker
What to Pub/ Sub?
GSM
  Bringing GSM up using APN codes – Auto detection
API
Send
Receive
CAN health Check
Startup
HIVE MQTT
Data Interface Engine
Compute function outputs – Hypothesis
  Ping test periodically
  GSM time for display
OTA
CAN Interface
MQTT interface
Pub/ Sub to HMI application
Comm to low level CAN API
Handle Event from HMI
Event to CAN
  HMI App
  Data Interface Engine
HMI
LVGL
Operating System
Yocto Linux
IMD
  Digital input output read
Cloud
Solar Irradiation – Mechanism to fetch this data
Logging
Event Management
Variable Mapping
Event Pub/ Sub
UI team for Graphic development
Image handling
License open source
Startup scheduling
Scheduling sequence of Data interface Engine and HMI app
  PWM for understanding the system state
Export longs
SW update
System Logger
CAN Dumps
Data Interface Engine logging
HMI logging*
HMI Team
Collaborative
TBD
CAN
  Generic CAN SEND/ RECEIVE API
  Schedule CAN Receive and Send
  CAN dumps
MQTT Broker
  Install HIVE MQTT broker
  Concept of DIE  HMI app MQTT messages
  DIE page numbers and HMI app must display the page
GSM
  Bring GSM up on iMX board
Wifi check
  Wifi connection from app
Log
  CAN Dumps
  DIE log
  HMI log

## Slide 5: Subcomponent -- SW subsets
DC Wall box – Connectivity proposal
CAN
CAN Dumps
Data Handling
MQTT
MQTT Broker
What to Pub/ Sub?
GSM
  Bringing GSM up using APN codes – Auto detection
API
Send
Receive
CAN health Check
Startup
HIVE MQTT
Data Interface Engine
Compute function outputs – Hypothesis
  Ping test periodically
  GSM time for display
OTA
CAN Interface
MQTT interface
Pub/ Sub to HMI application
Comm to low level CAN API
Handle Event from HMI
Event to CAN
  HMI App
  Data Interface Engine
HMI
LVGL
Operating System
Yocto Linux
IMD
  Digital input output read
Cloud
Solar Irradiation – Mechanism to fetch this data
Logging
Event Management
Variable Mapping
Event Pub/ Sub
UI team for Graphic development
Image handling
License open source
Startup scheduling
Scheduling sequence of Data interface Engine and HMI app
  PWM for understanding the system state
Export longs
SW update
System Logger
CAN Dumps
Data Interface Engine logging
HMI logging*
HMI Team
Collaborative
TBD
Workshop on Work package analysis (5th Sep): PJ-CSS, EHM-PD3-PJ3
Identified key work package
SW component discretization
Development Language
  Data Interface Engine – Python
  HMI – C++
MQTT broker
  HIVE MQTT
HMI
  LVGL

## Slide 6: 12-Oct Workshop Status
DC Wall box Status
CAN
  Robust test done for IMX send/ receive
    Ping pong communication between Pi and IMX8. 2ms for one round trip for one CAN frame
    Tested for 1 hour and 360000 frames were handled without any loss
  Communication with Charcon established.
  APIs are tested and CAN matrix internally implemented for all required signals
DIE – Data interface engine
  CAN and MQTT interface concept created and implemented.
  CAN signals from vSECC* and Charcon* were interpreted and processed data was sent back as CAN Frames
  DIE able to switch HMI pages via MQTT as per the CAN signal received.
HMI
  Screens: Initialization, Charging, Health Check, Ready to Charge, Device failure implemented
  MQTT broker and other dependencies installed in linux image
Hardware Interface – Digital I/O
  Digital input and output signals tested in IMX board
CAN send/ receive time
* CANOE test

## Slide 7: Data Interface Engine – State diagram
DC Wall box Status

## Slide 8: TO DO
DC Wall box Status
System integration
  Vehicle to be simulated in HIL environment for testing vSECC functionality
    Support required Vector VT Simulator
  Digital inputs
    DC contractor requires relays, as opto-coupler could not provide enough driving current
    IMD to be tested (possibly for high voltage)
      Test planned to be tested with low voltage
  Communication with vSECC to be established
Data Interface Engine
  Charging state to implemented
  Complete system integration test
  Cloud connectivity
HMI
  GSM

## Slide 9: Status – 7th Sep
DC Wall box – Connectivity proposal
CAN Frame dumps
System Sequence diagram
HMI app 2 pages
ToDo
Timeline planning and feature prioritization – Workshop with HMI 8th Sept planned
Porting developed SW artefacts to iMX board

## Slide 10: CAN
DC Wall box – Connectivity proposal
Socket CAN implementation using python CAN module
CAN Send and Receive using Threads
How much (Size) CAN dumps to log..?

## Slide 11: AWS – Cloud Connectivity
DC Wall box – Connectivity proposal
AWS Cloud
What to exchange with cloud?
  Charging Session
  Solar irradiation
  Logs – Data Interface Engine & HMI logs
  FOTA – SW update (Data Interface Engine & HMI)
  User Authentication
Cloud
  Solar Irradiation – Mechanism to fetch this data
  Export longs
  SW update
iMX Board
AWS Cloud
Weather API (Open Weather)
Solar Irradiation
Charging Session from IMX to AWS cloud
  Charging current & voltage, start & end time of charge session, etc TBD.. (Navneeth & Pritam)
  JSON format – Web socket – OCPP2.0.1 standard
  OCPP Python package (Poojitha)
Solar Irradiation
  AWS will fetch from Open Weather API based on request from iMX (Navneeth)
Comm between iMX – AWS cloud
  Charging session – OCPP - Websockets
  Logs export – End of charging session logs are updated to cloud - https
  Solar irradiation – https – REST API