## Slide 1: MQTT Pub/ Sub proposal – Data interface Engine, HMI

## Slide 2: Page Names and Messages
MQTT Pub - Sub
Topic Name:
ParentTopic: /DCWallbox/
SubTopic: /HMI/
MessageTopic: /PageName/<ScreenNames>
  /DCWallbox/HMI/ PageName
  Message <String>
MessageTopic:/PageName /BootPage //Bootpage will not be sent by DIE. It has to be received from Scheduler
MessageTopic:/PageName /AllPage
  Message:<HealthIcon>:<PlugStatus>:<CloudConnection>

## Slide 3: Page Names and Messages
MQTT Pub - Sub
MessageTopic:/PageName/DeviceFailure
  Message: "failure_has_occured"
MessageTopic:/PageName/MissingConfig
  Message: "confiuration_missing"
MessageTopic:/PageName/HealthCheck
  Message:<CableCheckStatus>:<PowerBoardStatus>:<HeartBeatMsg>
MessageTopic:/PageName /ReadyToCharge
  Message: "wallbox_ready_to_charge"

## Slide 4: Page Names and Messages
MQTT Pub - Sub
MessageTopic:/PageName /ChargingInitPage
  Message: “initializing_charging"
MessageTopic:/PageName/ChargingProgressPage
  Message:<SolarEnergy>:<GridEnergy>:<ySolarPwr>:<yGridPwr>:<xTime>:<TotCost>:<PauseTimer>:<StopEventAck>:<ChargingState>
  Message:<StopEvent>

## Slide 5: Message Value Tables
MQTT Pub - Sub
Page Name | Message | Values
AllPage | HealthIcon | 0 No icon 1 Red icon with exclamation 2 White icon with exclamation 3 Green icon
 | PlugStatus | 0 Not Plugged 1 Connected 2 Charging 3 Connection Error
 | CloudConnection | 0 Not Connected 1 Connected
HealthCheck | CableCheckStatus | 0 No Check 1 Checking 2 Good
 | PowerBoardStatus | 0 No Check 1 Checking 2 Good
 | HeartBeatMsg | 0 Checking 1 Good

## Slide 6: Message Value Tables
MQTT Pub - Sub
Page Name | Message | Values
ChargingProgressPage | SolarEnergy | Physical Value
 | GridEnergy | Physical Value
 | ySolarPwr | Physical Value
 | yGridPwr | Physical Value
 | xTime | Physical Value
 | TotCost | Physical Value
 | TimeHr | Physical Value
 | TimeMin | Physical Value
 | TimeSec | Physical Value
 | StopEventAck | 0 Event message NOT Received 1 Event message Received and Acknowledged
 | ChargingState | 0 Charging //Display Stop Button 1 Terminating 2 Charging Complete 3 Charger Unplugged
 | StopEvent | 0 Stop Event not Active 1 Stop Event Active