## Slide 2
Notes: When This page is displayed, the background boot up processes are running. This includes:
CAN Boot up
GSM Boot up
DIE Boot up
Once the bootup is successful, DIE will instruct HMI to go to the page required.
If no message for DIE is received within a specified time, HMI automatically moves to page 3.

## Slide 3
9:45 AM
CONNECTION ERROR
Guest
Robert Bosch St.
Wall Box Failure Detected
Call Service Center
!
Notes: Any Hardware or Software failure occurring switches to this page

## Slide 4
9:45 AM
NOT PLUGGED
Guest
Robert Bosch St.
Charger not Configured!
Please Configure the Charger
!
Notes: If Settings are not configured, this page is displayed. The iMx must send inoperative state to the v.SECC in this state

## Slide 5
9:45 AM
NOT PLUGGED
Guest
Robert Bosch St.
Health Check in Progress...
Cable :
Power Board:
Check
Good
Check
Good
Charger Ready! Please Plug in to start Charging
Notes: Immediately after the boot up is successful, iMx does a Cable check and Board check from CharCon side to determine the system health. Once the checks are done the display prompts the readiness of the charger.
Any Problem during the check makes the display go the slide 3 CONCERN: Cable check when charger is unplugged produces HV on the plug. So do we need this page?

## Slide 6
9:45 AM
CONNECTED
Guest
Robert Bosch St.
Connection Detected!
Initializing Device....
Notes: Once vehicle is plugged in this page is displayed. Display stays on this page while the following background processes takes place:
Initialization between EV and v.SECC
Cable-Check
Precharge

## Slide 7
9:45 AM
CHARGING
Guest
Robert Bosch St.
Cost on Grid per kWh: €0.39
Time Since charging Start
0h 1m 42s
Energy Consumed:
Solar 5.8 kWh Grid 1.1 kWh
Total Cost of Charging:
€ 0.43
STOP
Notes: Once pre-charge phase is complete and energy transfer is started, the DIE continuously feeds the following info:
Cumulative Solar Energy Consumed
Cumulative Grid Energy Consumed
% of solar and grid energy consumed (for pie chart)
Total Cost of Charging
Timing info (hr, min, sec)

## Slide 8
9:45 AM
CHARGING
Guest
Robert Bosch St.
Cost on Grid per kWh: €0.39
Energy Consumed:
Solar 20.3 kWh Grid 5.9 kWh
Time Since charging Start
0h 30m 24s
Total Cost of Charging:
€ 1.13
STOP
Notes: The charging session can be stopped anytime using the STOP button. When this is pressed, v.SECC requests EV to initiate charging termination.

## Slide 9
9:45 AM
CHARGING
Guest
Robert Bosch St.
Cost on Grid per kWh: €0.39
Energy Consumed:
Solar 32.4 kWh Grid 7.3 kWh
Time Since charging Start
0h 30m 24s
Total Cost of Charging:
€ 2.85
STOP
Notes: The charging session can be stopped anytime using the STOP button. When this is pressed, v.SECC requests EV to initiate charging termination.

## Slide 10
9:45 AM
CHARGING
Guest
Robert Bosch St.
Cost on Grid per kWh: €0.39
Energy Consumed:
Solar 41.3 kWh Grid 8.7 kWh
Time Since charging Start
0h 45m 15s
Total Cost of Charging:
€ 3.39
STOP
Notes: The charging session can be stopped anytime using the STOP button. When this is pressed, v.SECC requests EV to initiate charging termination.

## Slide 11
9:45 AM
CHARGING
Guest
Robert Bosch St.
Cost on Grid per kWh: €0.39
Energy Consumed:
Solar 41.3 kWh Grid 8.7 kWh
STOP
Time Since charging Start
0h 45m 15s
Total Cost of Charging:
€ 3.39
Notes: The charging session can be stopped anytime using the STOP button. When this is pressed, v.SECC requests EV to initiate charging termination.

## Slide 12
9:45 AM
CHARGING
Guest
Robert Bosch St.
Cost on Grid per kWh: €0.39
Energy Consumed:
Solar 45.9 kWh Grid 10.2 kWh
Time Since charging Start
0h 57m 38s
Total Cost of Charging:
€ 3.98
STOP
Notes: The charging session can be stopped anytime using the STOP button. When this is pressed, v.SECC requests EV to initiate charging termination.

## Slide 13
9:45 AM
CHARGING
Guest
Robert Bosch St.
Cost on Grid per kWh: €0.39
Energy Consumed:
Solar 50.3 kWh Grid 12.6 kWh
Time Since charging Start
1h 14m 27s
Total Cost of Charging:
€ 4.91
STOP
Notes: At any point if EV requests for termination of charging, display switches to slide 9

## Slide 14
9:45 AM
Guest
Robert Bosch St.
Cost on Grid per kWh: €0.39
Energy Consumed:
Solar 50.3 kWh Grid 12.6 kWh
CONNECTED
Time Since charging Start
1h 14m 27s
Total Cost of Charging:
€ 4.91
Terminating Charging Session
Notes: During the Charging termination, the following processes takes place:
Post charge phase of the charging session
Welding Check (if requested by EV)

## Slide 15
9:45 AM
Guest
Robert Bosch St.
Cost on Grid per kWh: €0.39
Energy Consumed:
Solar 50.3 kWh Grid 12.6 kWh
Charging Complete!
Please unplug the charger
CONNECTED
Time Since charging Start
1h 14m 27s
Total Cost of Charging:
€ 4.91
Notes: Once Post charge phase is completed and EV has unlocked the plug, display this page requesting user to unplug the charger

## Slide 16
9:45 AM
Guest
Robert Bosch St.
Cost on Grid per kWh: €0.39
Energy Consumed:
Solar 50.3 kWh Grid 12.6 kWh
Connector Unplugged!
Charging session Info updated to Cloud
NOT PLUGGED
Time Since charging Start
1h 14m 27s
Total Cost of Charging:
€ 4.91
Notes: Once user has unplugged the charger, display this page. Start a timeout counter to stay on this page for 2 mins and go to slide 12 after timeout.
Alternatively, user can slide the top slider down and press the home button (see slide 13) to immediately go to slide 12

## Slide 17
9:45 AM
NOT PLUGGED
Guest
Robert Bosch St.
Charger Ready! Please Plug in to start Charging
Notes: Default home page

## Slide 18
9:45 AM
NOT PLUGGED
Guest
Robert Bosch St.
Charger Ready! Please Plug in to start Charging
SW Update
v.SECC
CharCon
Master Control
Logs
Home
Notes: The slider in the top can be slid down to select various settings. These settings are greyed out and can be opened only on admin login

## Slide 19
9:45 AM
Guest
Robert Bosch St.
Login to View/Change System Settings
CAR PLUGGED
Cancel
User ID:
RB123
Password:
****
Q
W
E
R
T
Y
A
S
U
I
O
P
D
F
G
H
J
K
Z
X
C
V
B
?123
,
N
M
.
L
Notes: When the user icon or the greyed-out settings from slide 13 are clicked, the login page is prompted

## Slide 20
9:45 AM
NOT PLUGGED
Admin
Robert Bosch St.
Charger Ready! Please Plug in to start Charging
SW Update
v.SECC
CharCon
Master Control
Logs
Home
Notes: Once logged in, the settings are accessible

## Slide 21
9:45 AM
NOT PLUGGED
Robert Bosch St.
Checking for Software Updates....
SW Update
v.SECC
CharCon
Master Control
Logs
Home
Admin
Notes: When software update button is clicked, the wall box checks for update on the cloud

## Slide 22
9:45 AM
NOT PLUGGED
Robert Bosch St.
Installing Updates...
SW Update
v.SECC
CharCon
Master Control
Logs
Home
Admin
Notes: If Updates are present, this page is displayed with update progress

## Slide 23
9:45 AM
NOT PLUGGED
Robert Bosch St.
You are fully updated!
SW Update
v.SECC
CharCon
Master Control
Logs
Home
Admin
Notes: Once update is complete / no new updates found in slide 16, this page is displayed

## Slide 24
9:45 AM
NOT PLUGGED
Robert Bosch St.
Vehicle ID : –
Charging State : STANDBY
Charging Mode : UNKNOWN
v.SECC Settings
SW Update
v.SECC
CharCon
Master Control
Logs
Home
Admin
Notes: v.SECC related settings. Most info is available when vehicle is connected

## Slide 25
9:45 AM
Robert Bosch St.
Vehicle ID : 00-4A-B5-68-C7-13
Charging State : CHARGE
Charging Mode : SCHEDULED
v.SECC Settings
CHARGING
SW Update
v.SECC
CharCon
Master Control
Logs
Home
Admin
Notes: v.SECC infos when vehicle is connected. Note that the vehicle ID may not be sent in which case it will be just a ‘-’ like in slide 19

## Slide 26
9:45 AM
NOT PLUGGED
Robert Bosch St.
CharCon Settings
Maximum Grid Current Limit
Present Mode : SLEEP
Present Current Value : –
Present Current Value : –
16
A
SW Update
v.SECC
CharCon
Master Control
Logs
Home
Admin
Notes: CharCon settings. The Max grid current must be configured at least once before first start up.

## Slide 27
Maximum Grid Current Limit
Present Mode : ACTIVE
Present Current Value : 10.25 A
Present Voltage Value : 395.6 V
9:45 AM
Robert Bosch St.
16
A
CHARGING
CharCon Settings
SW Update
v.SECC
CharCon
Master Control
Logs
Home
Admin
Notes: During charging various charging signals can be displayed here

## Slide 28
9:45 AM
NOT PLUGGED
Robert Bosch St.
Master Control
Cost per kWh on Grid
Contactor Status : OPEN
0.39
Euros
SW Update
v.SECC
CharCon
Master Control
Logs
Home
Admin
Notes: Configuration of the cost per kWh on the grid must be done here. (at least once before first charging session)
The recommended cable check voltage for cable check in slide 4 (at least once before first charging session)
We can also manually trigger the cable check with the Start Cable Check button (Mainly for diagnostics if needed)
The Contractor status is also displayed

## Slide 29
Cost per kWh on Grid
Contactor Status : CLOSED
0.39
Euros
9:45 AM
Robert Bosch St.
Master Control
CHARGING
SW Update
v.SECC
CharCon
Master Control
Logs
Home
Admin
Notes: During Charging in input parameters and manual cable check are disabled.

## Slide 30
9:45 AM
NOT PLUGGED
Robert Bosch St.
Logs
Export Logs to Cloud
SW Update
v.SECC
CharCon
Master Control
Logs
Home
Admin
Notes: The system logs are displayed here. The logs can be exported to cloud.